## Slide 1: Combinational Circuits
Output is function of input only
  i.e. no feedback
  When input changes, output may change (after a delay)
•
•
•
•
•
•
n inputs
m outputs
Combinational
Circuits


## Slide 2: Combinational Circuits
Analysis
  Given a circuit, find out its function
  Function may be expressed as:
    Boolean function
    Truth table
Design
  Given a desired function, determine its circuit
  Function may be expressed as:
    Boolean function
    Truth table
?
?
?

## Slide 3: C A N O N I C A L FORM
Minterms (standard product)
A Boolean function can be expressed algebraically from a given truth table by forming a minterm(ANDed literals) for each combination of the variables that produces a 1 in the function and then taking the OR of all those terms
Maxterms (standard Sum)
It is important to note that
each maxterm is obtained from an OR term of n variables, with each variable being unprimed if the corresponding bit is a 0 and primed if a 1, and
each maxterm is the complement of its corresponding minterm and vice versa

## Slide 6
These examples demonstrate a second property of Boolean algebra: Any Boolean function can be expressed as a product of maxterms (with “product” meaning the ANDing of terms).

## Slide 7: Canonical form
Boolean functions expressed as a sum of minterms or product of maxterms are said to be in canonical form .
When a Boolean function is in its sum‐of‐minterms form, it is sometimes convenient to express the function in the following brief notation:

## Slide 8: Analysis Procedure
Truth Table Approach
= 1
= 1
= 1
= 1
= 1
= 1
= 1
= 1
= 1
= 1
= 1
= 1
1
1
1
1
1
1
0
0
1
A B C | F1 | F2
0 0 0 | 0 | 0
0 0 1 | 1 | 0
0 1 0 | 1 | 0
0 1 1 | 0 | 1
1 0 0 | 1 | 0
1 0 1 | 0 | 1
1 1 0 | 0 | 1
1 1 1 |  | 
1 1
 |  |  |  | B | 
 |  | 0 | 1 | 0 | 1
A |  | 1 | 0 | 1 | 0
 |  |  | C |  | 
 |  |  |  | B | 
 |  | 0 | 0 | 1 | 0
A |  | 0 | 1 | 1 | 1
 |  |  | C |  | 
F1=AB'C'+A'BC'+A'B'C+ABC
F2=AB+AC+BC

## Slide 9
NAND Logic
Example
Convert the circuit in the previous example to one that uses only NAND gates.
Recall from Boolean algebra that double inversion cancels. By adding inverting bubbles to above circuit, it is easily converted to NAND gates:
C
A
B
A
C
A
+
A
B
X =
Solution

## Slide 10
NAND gates are sometimes called universal gates because they can be used to produce the other basic Boolean functions.
Universal Gates
Inverter
A
A
AND gate
A
B
AB
A
B
A + B
OR gate
A
B
A + B
NOR gate

## Slide 11
NOR gates are also universal gates and can form all of the basic gates.
Universal Gates
Inverter
A
A
OR gate
A
B
A + B
A
B
AB
AND gate
A
B
AB
NAND gate

## Slide 12
Recall from DeMorgan’s theorem that AB = A + B. By using equivalent symbols, it is simpler to read the logic of SOP forms. The earlier example shows the idea:
NAND Logic
C
A
B
A
C
A
+
A
B
X =
The logic is easy to read if you (mentally) cancel the two connected bubbles on a line.

## Slide 13
NOR Logic
B
A
C
A
X =
Again, the logic is easy to read if you cancel the two connected bubbles on a line.
Alternatively, DeMorgan’s theorem can be written as A + B = A B. By using equivalent symbols, it is simpler to read the logic of POS forms. For example,
(A + B)(A + C)

## Slide 14: Design Procedure
Given a problem statement:
  Determine the number of inputs and outputs
  Derive the truth table
  Simplify the Boolean expression for each output
  Produce the required circuit
Example:
Design a circuit to convert a “BCD” code to “Excess 3” code
4-bits
0-9 values
4-bits
Value+3
?

## Slide 15: Design Procedure
BCD-to-Excess 3 Converter
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
 |  |  |  | C |  |  | 
 |  |  | 1 | 1 | 1 | B | 
A |  | x | x | x | x |  | 
 |  | 1 | 1 | x | x |  | 
 |  |  | D |  |  |  | 
 |  |  |  | C |  |  | 
 |  |  | 1 | 1 | 1 |  | 
 |  | 1 |  |  |  | B | 
A |  | x | x | x | x |  | 
 |  |  | 1 | x | x |  | 
 |  |  | D |  |  |  | 
 |  |  |  | C |  |  | 
 |  | 1 |  | 1 |  |  | 
 |  | 1 |  | 1 |  | B | 
A |  | x | x | x | x |  | 
 |  | 1 |  | x | x |  | 
 |  |  | D |  |  |  | 
 |  |  |  | C |  |  | 
 |  | 1 |  |  | 1 |  | 
 |  | 1 |  |  | 1 | B | 
A |  | x | x | x | x |  | 
 |  | 1 |  | x | x |  | 
 |  |  | D |  |  |  | 
w = A+BC+BD
x = B’C+B’D+BC’D’
y = C’D’+CD
z = D’

## Slide 16: Design Procedure
BCD-to-Excess 3 Converter
A B C D | w x y z
0 0 0 0 | 0 0 1 1
0 0 0 1 | 0 1 0 0
0 0 1 0 | 0 1 0 1
0 0 1 1 | 0 1 1 0
0 1 0 0 | 0 1 1 1
0 1 0 1 | 1 0 0 0
0 1 1 0 | 1 0 0 1
0 1 1 1 | 1 0 1 0
1 0 0 0 | 1 0 1 1
1 0 0 1 | 1 1 0 0
1 0 1 0 | x x x x
1 0 1 1 | x x x x
1 1 0 0 | x x x x
1 1 0 1 | x x x x
1 1 1 0 | x x x x
1 1 1 1 | x x x x
w = A + B(C+D)
x = B’(C+D) + B(C+D)’
y = (C+D)’ + CD
z = D’

## Slide 17: Seven-Segment Decoder
a
b
c
g
e
d
f
?
w
x
y
z
a
b
c
d
e
f
g
w x y z | a b c d e f g
0 0 0 0 | 1 1 1 1 1 1 0
0 0 0 1 | 0 1 1 0 0 0 0
0 0 1 0 | 1 1 0 1 1 0 1
0 0 1 1 | 1 1 1 1 0 0 1
0 1 0 0 | 0 1 1 0 0 1 1
0 1 0 1 | 1 0 1 1 0 1 1
0 1 1 0 | 1 0 1 1 1 1 1
0 1 1 1 | 1 1 1 0 0 0 0
1 0 0 0 | 1 1 1 1 1 1 1
1 0 0 1 | 1 1 1 1 0 1 1
1 0 1 0 | x x x x x x x
1 0 1 1 | x x x x x x x
1 1 0 0 | x x x x x x x
1 1 0 1 | x x x x x x x
1 1 1 0 | x x x x x x x
1 1 1 1 | x x x x x x x
 |  |  |  | y |  |  | 
 |  | 1 |  | 1 | 1 |  | 
 |  |  | 1 | 1 | 1 | x | 
w |  | x | x | x | x |  | 
 |  | 1 | 1 | x | x |  | 
 |  |  | z |  |  |  | 
BCD code
a = w + y + xz + x’z’
b = . . .
c = . . .
d = . . .

## Slide 18: Binary Adder
Half Adder
  Adds 1-bit plus 1-bit
  Produces Sum and Carry
HA
x
y
S
C
x y | C S
0 0 | 0 0
0 1 | 0 1
1 0 | 0 1
1 1 | 1 0
x
+ y
───
C S
x
y
S
C

## Slide 19: Binary Adder
Full Adder
  Adds 1-bit plus 1-bit plus 1-bit
  Produces Sum and Carry
x y z | C S
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 0 1
0 1 1 | 1 0
1 0 0 | 0 1
1 0 1 | 1 0
1 1 0 | 1 0
1 1 1 | 1 1
x
+ y
+ z
───
C S
FA
x
y
z
S
C
 |  |  |  | y | 
 |  | 0 | 1 | 0 | 1
x |  | 1 | 0 | 1 | 0
 |  |  | z |  | 
 |  |  |  | y | 
 |  | 0 | 0 | 1 | 0
x |  | 0 | 1 | 1 | 1
 |  |  | z |  | 
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z
C = xy + xz + yz

## Slide 20: Binary Adder
Full Adder
x
y
z
S
C
x
y
z
S
C
S = xy'z'+x'yz'+x'y'z+xyz = x  y  z
C = xy + xz + yz

## Slide 21: Binary Adder
Full Adder
x
y
z
S
C
HA
x
y
z
HA
S
C

## Slide 22: Binary Adder
c3 c2 c1 .
+ x3 x2 x1 x0
+ y3 y2 y1 y0
────────
Cy S3 S2 S1 S0
FA
x3 x2 x1 x0
FA
FA
FA
y3 y2 y1 y0
S3 S2 S1 S0
C4 C3 C2 C1
0
Binary Adder
x3x2x1x0 y3y2y1y0
S3S2S1S0
C0
Cy
Carry Propagate Addition

## Slide 23: 1 bit comparator

## Slide 24: Decoders
Extract “Information” from the code
Binary Decoder
  Example: 2-bit Binary Number
Binary Decoder
x1
x0
Only one lamp will turn on
0
0
1
0
0
0
1
0
2
3

## Slide 25: Decoders
2-to-4 Line Decoder
I1 I0 | Y3 Y2 Y1 Y0
0 0 | 0 0 0 1
0 1 | 0 0 1 0
1 0 | 0 1 0 0
1 1 | 1 0 0 0
Binary Decoder
I1
I0
y3
y2
y1
y0

## Slide 26: Decoders
3-to-8 Line Decoder
Binary Decoder
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0

## Slide 27: Decoders
“Enable” Control
Binary Decoder
I1
I0
E
Y3
Y2
Y1
Y0
E | I1 I0 | Y3 Y2 Y1 Y0
0 | x x | 0 0 0 0
1 | 0 0 | 0 0 0 1
1 | 0 1 | 0 0 1 0
1 | 1 0 | 0 1 0 0
1 | 1 1 | 1 0 0 0

## Slide 28: Decoders
Expansion
I2 I1 I0 | Y7 Y6 Y5 Y4 Y3 Y2 Y1 Y0
0 0 0 | 0 0 0 0 0 0 0 1
0 0 1 | 0 0 0 0 0 0 1 0
0 1 0 | 0 0 0 0 0 1 0 0
0 1 1 | 0 0 0 0 1 0 0 0
1 0 0 | 0 0 0 1 0 0 0 0
1 0 1 | 0 0 1 0 0 0 0 0
1 1 0 | 0 1 0 0 0 0 0 0
1 1 1 | 1 0 0 0 0 0 0 0
I2 I1 I0
Binary Decoder
I0
I1
E
Y3
Y2
Y1
Y0
Y7
Y6
Y5
Y4
Y3
Y2
Y1
Y0
Binary Decoder
I0
I1
E
Y3
Y2
Y1
Y0

## Slide 29: Implementation Using Decoders
Each output is a minterm
All minterms are produced
Sum the required minterms
Example: Full Adder
S(x, y, z) = ∑(1, 2, 4, 7)
C(x, y, z) = ∑(3, 5, 6, 7)
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
Binary Decoder
x
y
z
S C

## Slide 30: Implementation Using Decoders
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
Binary Decoder
x
y
z
S C
I2
I1
I0
Y7
Y6
Y5
Y4
Y3
Y2
Y1
Y0
Binary Decoder
x
y
z
S C

## Slide 31: Encoders
Put “Information” into code
Binary Encoder
  Example: 4-to-2 Binary Encoder
x3 x2 x1 | y1 y0
0 0 0 | 0 0
0 0 1 | 0 1
0 1 0 | 1 0
1 0 0 | 1 1
1
2
3
Binary Encoder
y1
y0
x1
x2
x3
Only one switch should be activated at a time

## Slide 32: Encoders
Octal-to-Binary Encoder (8-to-3)
I7 I6 I5 I4 I3 I2 I1 I0 | Y2 Y1 Y0
0 0 0 0 0 0 0 1 | 0 0 0
0 0 0 0 0 0 1 0 | 0 0 1
0 0 0 0 0 1 0 0 | 0 1 0
0 0 0 0 1 0 0 0 | 0 1 1
0 0 0 1 0 0 0 0 | 1 0 0
0 0 1 0 0 0 0 0 | 1 0 1
0 1 0 0 0 0 0 0 | 1 1 0
1 0 0 0 0 0 0 0 | 1 1 1
Binary Encoder
Y2
Y1
Y0
I7
I6
I5
I4 I3
I2
I1
I0

## Slide 33: Encoder / Decoder Pairs
Y2
Y1
Y0
I7
I6
I5
I4 I3
I2
I1
I0
I2
I1
I0
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
Binary Encoder
Binary Decoder
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0

## Slide 34: Multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
S1 S0 | Y
0 0 | I0
0 1 | I1
1 0 | I2
1 1 | I3

## Slide 35: Multiplexers
2-to-1 MUX
4-to-1 MUX
MUX
Y
I0
I1
S
MUX
Y
I0
I1
I2
I3
S1 S0

## Slide 36: Multiplexers
Quad 2-to-1 MUX
MUX
Y
I0
I1
S
MUX
Y
I0
I1
S
MUX
Y
I0
I1
S
MUX
Y
I0
I1
S
x3
x2
x1
x0
y3
y2
y1
y0
S
MUX
A3
A2
A1
A0
S E
Y3
Y2
Y1
Y0
B3
B2
B1
B0

## Slide 37: Implementation Using Multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
x y | F
0 0 | 1
0 1 | 1
1 0 | 0
1 1 | 1
Example F(x, y) = ∑(0, 1, 3)
x y
F
1
1
0
1

## Slide 38: Implementation Using Multiplexers
x y z | F
0 0 0 | 0
0 0 1 | 1
0 1 0 | 1
0 1 1 | 0
1 0 0 | 0
1 0 1 | 0
1 1 0 | 1
1 1 1 | 1
Example F(x, y, z) = ∑(1, 2, 6, 7)
MUX
Y
I0
I1
I2
I3 I4
I5
I6
I7
S2 S1 S0
x y z
0
1
1
0
0
0
1
1
F

## Slide 39: Implementation Using Multiplexers
MUX
Y
I0
I1
I2
I3
S1 S0
x y z | F
0 0 0 | 0
0 0 1 | 1
0 1 0 | 1
0 1 1 | 0
1 0 0 | 0
1 0 1 | 0
1 1 0 | 1
1 1 1 | 1
Example F(x, y, z) = ∑(1, 2, 6, 7)
x y
F
F = z
z
F = z
z
F = 0
0
F = 1
1

## Slide 40: Implementation Using Multiplexers
MUX
Y
I0
I1
I2
I3 I4
I5
I6
I7
S2 S1 S0
A B C D | F
0 0 0 0 | 0
0 0 0 1 | 1
0 0 1 0 | 0
0 0 1 1 | 1
0 1 0 0 | 1
0 1 0 1 | 0
0 1 1 0 | 0
0 1 1 1 | 0
1 0 0 0 | 0
1 0 0 1 | 0
1 0 1 0 | 0
1 0 1 1 | 1
1 1 0 0 | 1
1 1 0 1 | 1
1 1 1 0 | 1
1 1 1 1 | 1
Example F(A, B, C, D) = ∑(1, 3, 4, 11, 12, 13, 14, 15)
A B C
F
F = D
D
F = D
D
F = D
D
F = 0
0
F = 0
F = D
F = 1
F = 1
0
D
1
1

## Slide 41: Multiplexer Expansion
Y
I0
I1
I2
I3
I4
I5
I6
I7
S2 S1 S0
8-to-1 MUX using Dual 4-to-1 MUX
MUX
Y
I0
I1
I2
I3
S1 S0
MUX
Y
I0
I1
I2
I3
S1 S0
MUX
Y
I0
I1
S
0 0
1

## Slide 42: DeMultiplexers
DeMUX
I
Y3
Y2
Y1
Y0
S1 S0
S1 S0 | Y3 | Y2 | Y1 | Y0
0 0 | 0 | 0 | 0 | I
0 1 | 0 | 0 | I | 0
1 0 | 0 | I | 0 | 0
1 1 | I | 0 | 0 | 0

## Slide 43: Multiplexer / DeMultiplexer Pairs
Y
I7
I6
I5
I4 I3
I2
I1
I0
I
Y7
Y6
Y5
Y4 Y3
Y2
Y1
Y0
MUX
DeMUX
7
6
5
4
3
2
1
0
7
6
5
4
3
2
1
0
S2 S1 S0
S2 S1 S0
x2 x1 x0
y2 y1 y0
Synchronize

## Slide 44: DeMultiplexers / Decoders
Binary Decoder
I1
I0
E
Y3
Y2
Y1
Y0
E | I1 I0 | Y3 Y2 Y1 Y0
0 | x x | 0 0 0 0
1 | 0 0 | 0 0 0 1
1 | 0 1 | 0 0 1 0
1 | 1 0 | 0 1 0 0
1 | 1 1 | 1 0 0 0
DeMUX
I
Y3
Y2
Y1
Y0
S1 S0
S1 S0 | Y3 | Y2 | Y1 | Y0
0 0 | 0 | 0 | 0 | I
0 1 | 0 | 0 | I | 0
1 0 | 0 | I | 0 | 0
1 1 | I | 0 | 0 | 0