## Slide 1: Introduction Assembly Language Programming

## Slide 2: What is Assembly Language?
A low-level processor-specific programming language design to match the processor’s machine instruction set
Each assembly language instruction matches exactly one machine language instruction

## Slide 3: Why learn Assembly Language?
To learn how high-level language code gets translated into machine language
  i.e.: to learn the details hidden in HLL code
To learn the computer’s hardware
  by direct access to
    memory
    video controller
    sound card
    keyboard…
To speed up applications
  direct access to hardware (ex: writing directly to I/O ports instead of doing a system call)
  good ASM code is faster and smaller: rewrite in ASM the critical areas of code

## Slide 4: Assembly Language Applications
Application programs are rarely written completely in assembly language
  only time-critical parts are written in ASM
    An interface subroutine (called from HLL programs) is written in ASM for direct hardware access
    Device drivers (called from the OS)
ASM often used for embedded systems (programs stored in PROM chips)
    computer cartridge
    Games
    Microcontrollers (automobiles, industrial plants...)
    telecommunication equipment…
Very fast and compact but processor-specific

## Slide 5: Advantages of Assembly Language
Shows how program interfaces with the processor, operating system, and BIOS.
Shows how data is represented and stored in memory and on external devices.
Clarifies how processor accesses and executes instructions and how instructions access and process data.
Clarifies how a program accesses external devices.

## Slide 6: Reasons for using Assembly Language
A program written in Assembly Language requires considerably less memory and execution time than one written in a high –level language.
Assembly Language gives a programmer the ability to perform highly technical tasks that would be difficult, if not impossible in a high-level language.
Although most software specialists develop new applications in high-level languages, which are easier to write and maintain, a common practice is to recode in assembly language those sections that are time-critical.
Resident programs (that reside in memory while other program execute) and interrupt service routines (that handle input and output) are almost always develop in Assembly Language.

## Slide 7: Comparison of Assembly Language and High-Level Languages
Type of Applications | High-Level Language | Assembly Language
Business application software for single platform. | Formal structures make it easy to organize and maintain. | No formal structure.
Hardware device driver. | Awkward coding techniques required. | Hardware access is straightforward and simple.
Business application for multiple platforms. | Portable. | Difficult to maintain.
Embedded systems and computer games requiring direct hardware access. | Produces too much executable code, and may not run efficiently. | Ideal, because the executable code is small and runs quickly.

## Slide 8: Machine Language
An assembler is a program that converts ASM code into machine language code:
  mov al,5 (Assembly Language)
  1011000000000101 (Machine Language)
    most significant byte is the opcode for “move into register AL”
    the least significant byte is for the operand “5”
Directly programming in machine language offers no advantage (over Assembly)...

## Slide 9: Assembly Language Model
…
add r1,r2
sub r2,r3
cmp r3,r4
bne I1
sub r4,1
I1: jmp I3
…
ALU
PC
Registers
Memory

## Slide 10: Assembly Language Instructions
Built from two pieces
Add R1, R3, 3
Opcode
What to do with the data
(ALU operation)
Operands
Where to get data and put the results

## Slide 11: Types of Opcodes
Arithmetic, logical
  add, sub, mult
  and, or
  Cmp
Memory load/store
  ld, st
Control transfer
  jmp
  bne
Complex
  movs

## Slide 12: Operands
Each operand taken from a particular addressing mode:
Examples:
Register add r1, r2, r3
Immediate add r1, r2, 10
Indirect mov r1, (r2)
Offset mov r1, 10(r3)
PC Relative beq 100
Reflect processor data pathways

## Slide 13: Types of Assembly Languages
Assembly language closely tied to processor architecture
At least four main types:
CISC : Complex Instruction-Set Computer
RISC : Reduced Instruction-Set Computer
DSP : Digital Signal Processor
VLIW : Very Long Instruction Word

## Slide 14: CISC Assembly Language
Developed when people wrote assembly language
Complicated, often specialized instructions with many effects
Examples from x86 architecture
  String move
  Procedure enter, leave
Many, complicated addressing modes
So complicated, often executed by a little program (microcode)

## Slide 15: RISC Assembly Language
Response to growing use of compilers
Easier-to-target, uniform instruction sets
“Make the most common operations as fast as possible”
Load-store architecture:
  Arithmetic only performed on registers
  Memory load/store instructions for memory-register transfers
Designed to be pipelined

## Slide 16: DSP Assembly Language
Digital signal processors designed specifically for signal processing algorithms
Lots of regular arithmetic on vectors
Often written by hand
Irregular architectures to save power, area
Substantial instruction-level parallelism

## Slide 17: VLIW Assembly Language
Response to growing desire for instruction-level parallelism
Using more transistors cheaper than running them faster
Many parallel ALUs
Objective: keep them all busy all the time
Heavily pipelined
More regular instruction set
Very difficult to program by hand
Looks like parallel RISC instructions

## Slide 18: Types of Assembly Languages

## Slide 19: The Computer Organization - INTEL PC
In this course, only INTEL assembly language will be learnt. Below is a brief description of the development of a few INTEL model.
(i) 8088
  Has 16-bit registers and 8-bit data bus
  Able to address up to 1 MB of internal memory
  Although registers can store up to 16-bits at a time but the data bus is only able to transfer 8 bit data at one time
(ii) 8086
  Is similar to 8088 but has a 16-bit data bus and runs faster.

## Slide 20
(iii) 80286
  Runs faster than 8086 and 8088
  Can address up to 16 MB of internal memory
  multitasking => more than 1 task can be ran
  simultaneously
(iv) 80386
  has 32-bit registers and 32-bit data bus
  can address up to 4 billion bytes. of memory
  support “virtual mode”, whereby it can swap portions of memory onto disk: in this way, programs running concurrently have space to operate.
(v) 80486
  has 32-bit registers and 32-bit data bus
  the presence of CACHE

## Slide 21
(vi) Pentium
  has 32-bit registers, 64-bit data bus
  has separate caches for data and instruction
  the processor can decode and execute more than one
  instruction in one clock cycle (pipeline)
(vii) Pentium II & III
  has different paths to the cache and main memory

## Slide 22
In performing its task, the processor (CPU) is partitioned into two logical units:
1) An Execution Unit (EU)
2) A Bus Interface Unit (BIU)
EU
  EU is responsible for program execution
  Contains of an Arithmetic Logic Unit (ALU), a Control Unit (CU) and a number of registers
BIU
  Delivers data and instructions to the EU.
  manage the bus control unit, segment registers and instruction queue.
  The BIU controls the buses that transfer the data to the EU, to memory and to external input/output devices, whereas the segment registers control memory addressing.

## Slide 23
EU and BIU work in parallel, with the BIU keeping one step ahead. The EU will notify the BIU when it needs to data in memory or an I/O device or obtain instruction from the BIU instruction queue.
When EU executes an instruction, BIU will fetch the next instruction from the memory and insert it into to instruction queue.

## Slide 24
AH AL
BH BL
CH CL
DH DL
SP
BP
SI
DI
AX
CX
DX
BX
EU : Execution Unit
BIU : Bus Interface Unit
CS
Program Control
DS
SS
ES
ALU
CU
Flag register
1
2
3
Bus Control Unit
4
n
Bus
Instruction Pointer
Instruction Queue
(Program Counter)

## Slide 25: Segment And Addressing
Segments are special areas in the memory that is defined in a program, containing the code, data, and stack.
The segment position in the memory is not fixed and can be determined by the programmer
3 main segments for the programming process:
(i) Code Segment (CS)
Contains the machine instructions that are to execute.
Typically, the first executable instruction is at the start of this segment, and the operating system links to that location to begin program execution.
CS register will hold the beginning address of this segment

## Slide 26
(ii) Data Segment (DS)
Contains program’s defined data, constants and works areas.
DS register is used to store the starting address of the DS
(iii) Stack Segmen (SS)
Contains any data or address that the program needs to save temporarily or for used by your own “called”subroutines.
SS register is used to hold the starting address of this segment

## Slide 27
Address
Address
Address
Stack segment
Data segment
Code segment
Contains the beginning address of each segment
Segment register
(in CPU)
memory
(MM)
SS Register
DS Register
CS Register

## Slide 28: Registers
Registers are used to control instructions being executed, to handle addressing of memory, and to provide arithmetic capability
Registers of Intel Processors can be categorized into:
  Segment register
  Pointer register
  General purpose register
  Index register
  Flag register

## Slide 29: i) Segment register
There are 6 segment registers :
CS register
Contains the starting address of program’s code segment.
The content of the CS register is added with the content in the Instruction Pointer (IP) register to obtain the address of the instruction that is to be fetched for execution.
(Note: common name for IP is PC (Program Counter))
(b) DS register
Contains the starting address of a program’s data segment.
The address in DS register will be added with the value in the address field (in instruction format) to obtain the real address of the data in data segment.

## Slide 30
(c) SS Register
Contains the starting address of the stack segment.
The content in this register will be added with the content in the Stack Pointer (SP) register to obtain the required word.
ES (Extra Segment) Register
Used by some string (character data) operations to handle memory addressing
ES register is associated with the Data Index (DI) register.
(e) FS and GS Registers
Additional extra segment registers introduced in 80386 for handling storage requirement.

## Slide 31: (ii) Pointer Registers
There are 3 pointer registers in an Intel PC :
Instruction Pointer register
The 16-bit IP register contains the offset address or displacement for the next instruction that will be executed by the CPU
The value in the IP register will be added into the value in the CS register to obtain the real address of an instruction

## Slide 32
Example :
The content in CS register = 39B40H
The content in IP register = 514H
next instruction address: 39B40H
+ 514H
. 3A054H
Intel 80386 introduced 32-bit IP, known as EIP (Extended IP)

## Slide 33
(b) Stack Pointer Register (Stack Pointer (SP))
  The 16-bit SP register stores the displacement value that will be combined with the value in the SS register to obtain the required word in the stack
  Intel 80386 introduced 32-bit SP, known as ESP (Extended SP)
Example:
Value in register SS = 4BB30H
Value in register SP = + 412H
4BF42H
(c) Base Pointer Register
The 16-bit BP register facilitates referencing parameters, which are data and addresses that a program passes via a stack
The processor combines the address in SS with the offset in BP

## Slide 34
(iii) General Purpose Registers
There are 4 general-purpose registers, AX, BX, CX, DX:
(a) AX register
Acts as the accumulator and is used in operations that involve input/output and arithmetic
The diagram below shows the AX register with the number of bits.
8 bit
8 bit
32 bits
AH
AL
AX
EAX
EAX : 32 bit
AX : 16 bit (rightmost 16-bit portion of EAX)
AH : 8 bit => leftmost 8 bits of AX (high portion)
AL : 8 bit => rightmost 8 bit of AX (low portion)

## Slide 35
(b) BX Register
o Known as the base register since it is the only this general purpose register that can be used as an index to extend addressing.
o This register also can be used for computations
o BX can also be combined with DI and SI register as a base registers for special addressing like AX, BX is also consists of EBX, BH and BL
8 bit
8 bit
32 bits
BX
EBX
BH
BL

## Slide 36
(c) CX Register
known as count register
may contain a value to control the number of times a loops is repeated or a value to shift bits left or right
CX can also be used for many computations
Number of bits and fractions of the register is like below :
8 bit
8 bit
32 bits
CX
CH
CL
ECX

## Slide 37
(d) DX Register
Known as data register
Some I/O operations require its use
Multiply and divide operations that involve large values assume the use of DX and AX together as a pair to hold the data or result of operation.
Number of bits and the fractions of the register is as below :
8 bit
8 bit
32 bits
DX
DH
DL
EDX

## Slide 38
(iv) Index Register
There are 2 index registers, SI and DI
(a) SI Register
o Needed in operations that involve string (character) and is always usually associated with the DS register
o SI : 16 bit
o ESI : 32 bit (80286 and above)
(b) DI Register
o Also used in operations that involve string (character) and it is associated with the ES register
o DI : 16 bit
o EDI : 32 bit (80386 and above)

## Slide 39
(v) FLAG Register
o Flags register contains bits that show the status of some activities
o Instructions that involve comparison and arithmetic will change the flag status where some instruction will refer to the value of a specific bit in the flag for next subsequent action
- 9 of its 16 bits indicate the current status of the computer
and the results of processing
- the above diagram shows the stated 9 bits
O
D
I
T
S
Z
A
P
C
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0

## Slide 40
O
D
I
T
S
Z
A
P
C
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
OF (overflow): indicate overflow of a high-order (leftmost) bit following arithmetic
DF (direction): Determines left or right direction for moving or comparing string (character) data
IF (interrupt): indicates that all external interrupts such as keyboard entry are to be processed or ignored
TF (trap): permits operation of the processor in single-step mode. Usually used in “debugging” process
SF (sign): contains the resulting sign of an arithmetic operation (0 = +ve, 1 = -ve)
ZF (zero): indicates the result of an arithmetic or comparison operation (0 = non zero; 1 = zero result)
AF (auxillary carry): contains a carry out of bit 3 into bit 4 in an arithmetic operation, for specialized arithmetic
PF (parity): indicates the number of 1-bits that result from an operation. An even number of bits causes so-called even parity and an odd number causes odd parity
CF (parity): contains carries from a high-order (leftmost) bit following an arithmetic operation; also, contains the content of the last bit of a shift or rotate operation.